## Slide 1
Cyclic Voltammetry
Cyclic voltammetry (CV) is a powerful and popular electrochemical technique commonly employed to investigate the reduction and oxidation processes of molecular species.
CV measures the current arises due to oxidation or reduction in an electrochemical cell under conditions where voltage is in excess of that predicted by Nernst equation.
In CV measurements 3 electrodes are used namely, working electrode, counter electrode and reference electrode
In CV the potential is scanned over a known range. The scanning is performed with a speed known as scan rate. The current is measured as the voltage is scanned. Thus, when there is a reduction or oxidation the current would increase.
The potential of the working electrode is measured against the reference potential which maintains a constant potential
*
The * denotes the switching potential which is the point where the voltage is sufficient enough to cause oxidation or reduction of an analyte.
The potential is scanned both forward and backward direction

## Slide 2
FC -Ferrocene
Co(Cp)-cobalt cyclopentadienyl
FC+ -oxidized Ferrocene
The Nernst equation provides a powerful way to predict how a system will respond to a change of concentration of species in solution or a change in the electrode potential
If a potential of E = E°′ ≈ E1/2 is applied to the Fc+ solution, the Nernst equation predicts that Fc+ will be reduced to Fc until [Fc+] = [Fc], and equilibrium is achieved.
When the potential is scanned during the CV experiment, the concentration of the species in solution near the electrode changes over time in accordance with the Nernst equation

## Slide 3
If the reduction process is chemically and electrochemically reversible, the difference between the anodic and cathodic peak potentials, called peak-to-peak separation (ΔEp), is 57 mV at 25 °C (2.023 RT/F)
Chemical reversibility is used to denote whether the analyte is stable upon reduction and can subsequently be reoxidized.
When there is a low barrier to electron transfer (electrochemical reversibility), the Nernstian equilibrium is established immediately upon any change in applied potential. By contrast, when there is a high barrier to electron transfer (electrochemical irreversibility), electron transfer reactions are sluggish and more negative (positive) potentials are required to observe reduction (oxidation) reactions, giving rise to larger ΔEp
Mass Transport
Movement of the analyte to the electrode surface is controlled by three modes of mass transport:
Convection : Due to mechanical forces (stirring)
Migration: Ionic species move due to electric field (electrostatic attraction between ions and electrode)
Diffusion: analyte movements occurs due to difference in concentration (high to low)
The two peaks are separated due to diffusion of the analyte to and from the electrode

## Slide 4
Scan rate
The scan rate of the experiment controls how fast the applied potential is scanned. Faster scan rates lead to a decrease in the size of the diffusion layer; as a consequence, higher currents are observed.
For electrochemically reversible electron transfer processes involving freely diffusing redox species, the Randles−Sevcik equation
Randles−Sevcik equation
Randles−Sevcik equation describes how the peak current ip (A) increases linearly with the square root of the scan rate  (V s−1),
n is the number of electrons transferred in the redox event,
A (cm2) is the electrode surface area (geometric surface area),
Do (cm2 s−1) is the diffusion coefficient of the oxidized analyte,
and C0 (mol cm−3) is the bulk concentration of the analyte
For an electrochemically reversible electron transfer processes involving freely diffusing redox species, the equation predicts dependence of peak current on scan rate and the plot of ip versus 1/2 should be linear.

## Slide 5
For an electrode adsorbed species the current response is given by
The current response for an adsorbed species is expected to be linear with .
Deviation in the ip Vs 1/2 is noted for quasi reversible or electron transfer occurring via surface adsorbed species. This can be distinguished from the peak-to-peak separation.
For surface adsorbed species no peak-to-peak separation is noted.
Randles−Sevcik equation can be used to determine
Diffusion coefficient
Electrochemical active area of the electrode
Concentration of the redox species

## Slide 6
Electrochemical cell for a CV experiment
As electron transfer occurs during a CV experiment, electrical neutrality is maintained via migration of ions in solution. As electrons transfer from the electrode to the analyte, ions move in solution to compensate the charge and close the electrical circuit.
A salt, called a supporting electrolyte, is dissolved in the solvent to help decrease the solution resistance. The mixture of the solvent and supporting electrolyte is commonly termed the “electrolyte solution.”
Solvent
1. It is liquid at experimental temperatures.
2. It dissolves the analyte and high concentrations of the
supporting electrolyte completely.
3. It is stable toward oxidation and reduction in the potential
range of the experiment.
4. It does not lead to deleterious reactions with the analyte or
supporting electrolyte.
Dry solvent-Dichloromethane, acetonitrile
Tetraalkylammonium salts, NaClO4
Supporting electrolyte
1. It is highly soluble in the solvent chosen.
2. It is chemically and electrochemically inert in the
conditions of the experiment.
3. It can be purified

## Slide 7
In Biology
Most mechanisms which control biological functions (like cell respiration and photosynthesis) involve redox processes.
In photosynthesis: Electron carriers like iron-sulfur proteins, cytochromes and blue copper proteins provide a means of electron transport , which is triggered by the light absorption.
The overall process occurring in photosynthesis is
Reduction of carbon dioxide to carbohydrates
(photosystem I)
6CO2 + 6H2O  C6H12O6 + 6O2
6CO2 + 24H+ + 24e-  C6H12O6 + 6H2O
Oxidation of water to dioxygen
(photosystem II)
6H2O  6O2 + 24H+ + 24e-

## Slide 8
Difficulties in studying electrochemistry with biological systems
Slow rate of diffusion- less Faradaic current
Electroactive species present inside the protein chain-direct exchange is difficult
Adsorption of protein to surface- sometimes cause poisoning of electrode
The electron transfer processes depend on
Distance between redox centres
Structural changes concomitant with the electron transfer
Spatial disposition of the protein with respect to electrode surface

## Slide 9
Cytochromes (Iron-porphyrin based heme protein)
Classified depending on the heme type
Addition of one electron corresponding to Fe3+/Fe2+ reduction hardly alters the structure of the octahedral coordination sphere of the Fe centre. However, due to protonation/deprotonation due to electron transport structural alterations occur at the peripheral.
With direct electro-reduction of the Fe(III)/Fe(II), it is important to keep in mind that cytochrome c, at pH 7, in the oxidised state has an overall charge of + 7.5, whereas in the reduced state it has a charge of +6.5. (the charges are due to COO- and NH3+ groups of aminoacids and metals.
Protein immobilized on the SnO2 electrode
Au electrode pretreated with bipyridyl and protein in solution

## Slide 10
the reduction process is really reversible (Eo = + 0.26 V vs. NHE)
In Figure (a) the current is expected to increase linearly with the scan rate, whereas in the case of simple diffusion, Figure (b) the current increases linearly with the square root of the scan rate
Since oxidized cytochrome c, at pH 7, has an overall positive charge of +7.5, it means that it bears an excess of NH3+ groups.
The activated complex formed through hydrogen bonds between the lysine groups of the protein and the pyridyl nitrogen atoms adsorbed on the electrode surface, is thought to provide a good route for the rapid exchange of electrons.
The formation of the activated complex is confirmed by performing the measurement at pH 4, where the pyridyl nitrogen atoms are expected to be protonated. Indeed, no electrochemical activity is noted.
Cytochromes (Iron-porphyrin based heme protein)

## Slide 11
Fe-Sulfur proteins (non heme)
Rubredoxins : FeS4 assembly, consisting of an Fe(III) ion coordinated to four cysteine groups.
Total negative charge of -13 at pH 7 (pI = 3)
Graphite electrode does not favour the electrostatic interaction between the electrode surface and the protein.
use of positively charged additives (Mg2+ salts, [Cr(NH3)63+] compensate the negative charge of the electrode.
Rubredoxins have Eo values for the Fe(III)/Fe(II) reduction
range from +0.05 V to -0.05 V vs.NHE
CV measured in the (a) absence and (b) presence of [Cr(NH3)63+]